## Slide 1: Topology and L3 network service relation proposal

## Slide 2: Example network
Node PE-1
Node PE-2
Node P-A
Customer Site A
Customer Site B
Service provider domain

## Slide 3
L1-node-topology
PE-1
P-A
UNI-Topology
PE-2
Node PE-1
VPN node
Node PE-2
VPN node
Bearer
Bearer
TP-1
TP-2
Bearer can have a leafref to a TP of the topology
VPN node can have a reference to the node of a topology
Supporting node
Supporting node
TP-1
TP-2
UNI topology contains just PE nodes and client interfaces (UNIs)

## Slide 4: Proposal
+--rw vpn-nodes
| +--rw vpn-node* [vpn-node-id ne-id]
| +--rw vpn-node-id string
| +--rw description? string
| +--rw topo-node? -> /nw:networks/network/node/node-id
Add a reference to the node (as in IETF-topology) to link vpn-nodes and PE node
Add supporting-termination-point (as in IETF-topology) to link bearer and interface of the PE
| | +--rw bearer
| | | +--rw bearer-reference? string {bearer-reference}?
| | | +--rw uni-reference? -> /nw:networks/network/node/termination-point/tp-id

## Slide 5: Questions
For the UNI-topology, basic IETF topology is enough? L3? Augmentation of IETF topology?